## Slide 1: Graph Programming Model Efficient Approach For Sensor Signal Processing
Mr. Steve Kirsch
Principal Fellow
Raytheon Space and Airborne Systems
9/10/2012
Copyright © 2012 Raytheon Company. All rights reserved.
Customer Success Is Our Mission is a registered trademark of Raytheon Company.

## Slide 2: Agenda
Graph Programming Model (GPM) goals
Overview of GPM basics
GPM hierarchical program structure
A brief look at how GPM achieves efficiency
Conclusion and Path Forward

## Slide 3: Key Goals Of The Graph Programming Model (GPM)
Goals
  Efficiency
  Portability
  Scalability
  Productivity
Efficiency – High throughput without exposing processing target details thus maintaining a clean programming abstraction
Portability – Require no or minimal application software modifications when target hardware is upgraded or application is move to a significantly different target architecture
Scalability – Provide increased application performance with no application modification as target hardware capabilities increase
Productivity – Provide process and tools that reduce the complexities of developing a highly efficient parallel program

## Slide 4: GPM: Basic Concept of Operation
GPM utilizes Directed Acyclic Graphs (DAGs) as the basic building block
  Collection of vertices and directed edges
  Each edge connects one vertex to another, such that there is no way to start at a vertex and follow a sequence of edges that eventually loops back to the same vertex
  A precedence relationship is established by the data flow pattern

## Slide 5: Agenda
Graph Programming Model (GPM) goals
Overview of GPM basics
GPM hierarchical program structure
A brief look at how GPM achieves efficiency
Conclusion and Path Forward

## Slide 6: GPM: Basic Concept of Operation DAGs Used To Express Data Level Parallelism (DLP)
Datasets
  Represents multi-dimensional data (eg Radar sensor fast time samples across a row, slow time (pulse to pulse samples) down a column)
  Typically data dependencies exist in one dimension (or few dimensions) and expose data level parallelism in the other dimensions
JobClasses
  SPMD processing model
  JobClasses are designed to consume data level parallelism
JobClass Views
  Data parallelism description
Single Program
Multiple Data
SPMD Machine
Dataset 1
D1.0
D1.1
D1.n
-
1
D1.n
Dataset 2
D2.0
D2.1
D2.n
-
1
D2.n
SPMD
1.0
1.1
1.n
-
1
1.n
JobClass
GPM Explicitly Exposes Algorithmic DLP
SPMD

## Slide 7: GPM: Basic Concept of Operation DAGs Used To Express Thread Level Parallelism (TLP)
SubGraphs
  JobClasses are grouped into a subGraph
  A set of subGraphs forms an MPMD machine
  Subgraphs are separately allocatable processing threads
  Datasets consumed by a subgraph are allocated to memory local to where the subgraph executes
  SubGraphs can be allocated to processing resources in real time
2
n
-
1
n
Datasets
Datasets
D0
D1
DN
-
1
DN
Dn+2
Dn+3
DM
-
1
DM
SubGraph
GPM Explicitly Exposes Algorithmic TLP

## Slide 8: GPM: Basic Concept of Operation JobClass Views Express Data Reorganization
JobClass View
  Expresses how data is access by each vertex
  The view describes a virtually contiguous subset of the dataset
A JobClass view can express any arbitrary reorganization of the data
  Typically used for transposing data between sequential processing stages
1.0
1.1
1.n
-
1
1.n
2.0
2.1
2.n
-
1
2.n
Dataset
D1.0
D1.1
D1.n
-
1
D1.n
Dataset
D3.0
D3.1
D3.n
-
1
D3.n
Dataset
D2.0
D2.1
D2.n
-
1
D2.n
JobClass
JobClass
Data Reorganization is Systematically Handled in GPM

## Slide 9: Agenda
Graph Programming Model (GPM) goals
Overview of GPM basics
GPM hierarchical program structure
A brief look at how GPM achieves efficiency
Conclusion and Path Forward

## Slide 10: GPM: Hierarchical Program Structure Graphs are the fundamental building blocks
Graphs are used as building blocks to construct a signal processing application
  Graphs are reusable DAGs that can be parameterized (eg number of collected samples to process, number of pulses to process, etc)
SAR (Synthetic Aperture Radar ) signal processing example
  A single PtP (Pulse to Pulse) graph type is used for processing segments of a long coherent collection
  Batch Graph for integrating the PtP outputs where data dependences exist between the pulse to pulse graphs
  Multiple PtP Graphs maybe processed in parallel when collection time < processing time
Graph are used to express a course gain inherent algorithm TLP

## Slide 11: GPM: Hierarchical Program Structure Graphs are decomposed into Subgraphs
Subgraphs represent a finer gain expression of TLP
  Independent grouping of data and processing
  May execute in parallel thus utilizing parallel processing resources
    Provides an opportunity to manage processing latency
  Inter-subgraph communication implementation can utilize message passing
    Typical for a loosely coupled memory hierarchy

## Slide 12: GPM: Hierarchical Program Structure Subgraphs are decomposed Into Jobclasses
Subgraphs are composed into one or more Jobclasses
Jobclasses are SPMD (shown on an earlier chart) that consume the DLP that exists in datasets
A Jobclass consists of one or more Jobs
  Each Job may execute in parallel on a cluster of processing nodes allocated to the subGraph
  If a jobclass contains more Jobs then processing nodes than jobs will be queued and execute sequentially

## Slide 13: GPM: Hierarchical Program Structure Dataset are decomposed into Tiles
Dataset is divided into tiles exposing Data Level Parallelism (DLP)
A Jobclass view defines how to carve up the dataset into tiles
  Tiles represent virtually contiguous chunks of data that can be processed in parallel
  Typically there are 100s of tiles that comprise a dataset
Tiles are grouped and assigned to Jobs
  Jobs process tiles in parallel
  A single job processes its tiles sequentially
Number of Dimensions
Atomic Dimension
  Number of dimension required to access a tile
Dimension structure
  Length
  Stride
Job Class View Attributes

## Slide 14: Agenda
Graph Programming Model (GPM) goals
Overview of GPM basics
GPM hierarchical program structure
A brief look at how GPM achieves efficiency
Conclusion and Path Forward

## Slide 15: GPM Achieves Efficiency: By Using Data tiling
Tile 2
Ability to simultaneously move data and perform useful computation is key to high performance
  Job Sequencing and Data tiling provides the ability to bury data movement
Middleware
Tile 0
Tile 1
Tile 2
Tile 3
Tile 4
Tile 5
Tile 6
Tile 7
Dataset
Job 0
Job 1
Graph Controls
Spawns Graph
Queues Jobs
Waits for inputs
Dataset complete
Calls Begin
Calls Compute0
Calls Compute1
Calls Compute2
Calls Compute3
Calls End
Tile 0
Tile 4
Tile 1
Tile 5
Tile 0
Tile 4
Input
Buffers
Output
Buffers
Input
Buffers
Output
Buffers
Tile 1
Tile 1
Tile 5
Tile 5
Tile 2
Tile 3
Tile 3
Tile 6
Tile 6
Tile 7
Tile 7

## Slide 16: GPM Achieves Efficiency: Utilizing Heterogeneous Processing
Heterogeneous processing transparently integrated into the GPM
  Achieving performance/SWAP requires the flexibility of a variety of processor types
    Multi-core GP GPGPUs
    Multi-core SIMD arrays FPGAs
Key to transparent integration is a consistent API across processor types
  Exploiting TLP and DLP with a consistent interface
  Communication between processor types utilizing a consistent user abstraction
GPM achieve this by parameterizing the processor type
  Graph description simple references a processor type
  Allows an implementation to allocate the processing step to the appropriate resource
  Signal Processing within a JobClass utilizes a custom library assigned processor type
JobClass Description

## Slide 17: GPM Achieves Efficiency: Utilizing The Optimal Transport
Many signal processing problems are too large for a single SWAP constrained SMP machine thus requires a hybrid of SMP and message passing
  Partitioning a design to best utilizing the optimal transport is a function of the TLP available in an algorithm
  GMP exposes TLP is a systematic way that enables a runtime implementation to select the appropriate transport without impact to the signal processing design
  Intra-subgraph dataset utilize SMP communication
  Inter-subgraph dataset utilize message passing
Graph Description

## Slide 18: GPM Achieves Efficiency: By Variety Of Other Mechanisms
Coarse scale real time load balancing
  Coarse level load balancing is enable by use of subgraphs
  Subgraphs are independent so that they can be allocated in real time to the next available processing “Cluster” (Cluster is a group of SMP coupled machines)
Fine scale real time load balancing
  Data processed by a JobClass is partitioned between Jobs which at run time are allocated to processing nodes
  Work can be evenly spread across all the nodes within a cluster
Data locality control
  Since subgraphs are allocated to a cluster a runtime implementation can push dataset to the memory where the data will be consumed
  Dataset writes are executed in parallel with tile compute cycles so the data movement can buried
Data Alignment
  Efficient use of modern processors is typically sensitive to alignment of data to a fundamental hardware architecture constraint (e.g. cache line size)
  GPM parameterizes this fundament constraint which enforce data movement between JobClasses and datasets to be optimized for the target hardware

## Slide 19: GPM Efficiency Measured Results
Compute cycles and data IO transport time can be balanced thus reducing processing time verse unburied approaches
  Current runtime implementation measured over dozens of JobClasses showed a mix between memory bandwidth limited jobClasses and compute bound as a function of algorithmic processing step
  10% - 75% of the I/O time or compute cycle time can typically be buried
GPM implementation can achieve a low runtime overhead
  Typically 5% of total compute cycles
Heterogeneous processing comparison
  Results have shown that by carving out a few processing intense algorithms Performance/SWAP can be improved by more then 2x
  FPGA vs IBM Cell processor example
    IQ formation (FIR)
    IQ Calibration (Cross Coupled FIRs)
    Pulse Compressing (Fast Convolution)
    Motion Compensation (Phase ramp gen and complex multiple)

## Slide 20: Conclusions and Path Forward
Graph Programming Model achievement of goal can be directly associated with features of the architecture
  Discussed features of GPM that contribute to efficiency
  Portability, Scalability, Productivity features not discussed here are briefly described in the published paper Graph Programming Model: An Efficient Approach For Sensor Signal Processing
Runtime implementation of GPM has been characterized and has shown excellent results
Path Forward
  Add additional GPM features
    Data dependent cyclic behavior within a subgraph
  Continue to improve current implementation and development tool suite
    Performance model calculator
    Port runtime to multiple target platforms
    Addition of a GPGPU processor type
    Addition of a Graphical editor